A.
In the packet list pane, select the first DNS packet. In the packet detail pane, select the
User Datagram Protocol. The UDP hexdump will be highlighted in the packet byte lane.
Using the hexdump, Answer the following.(packet 49 of wsdata)
a. the source port number.	55720
b. the destination port number.	53
c. the total length of the user datagram.	76
d. the length of the data.	48 BYTES
e. whether the packet is directed from a client to a server or vice versa.	Client to server
f. the application-layer protocol.	UDP
g. whether a checksum is calculated for this packet or not.	Yes but unverified
B. What are the source and destination IP addresses in the DNS query message?
Src:172.16.59.45 Dst:172.16.19.201
What are those addresses in the response message?	Src and dst ip addresses
What is the relationship between the two?	The addresses are swapped in the response
C. What are the source and destination port numbers in the query message?
Src:55720	Dst:53
Which port number is a well-known port number?	DNS 53
D. What is the length of the first packet? How many bytes of payload are carried by the first packet?
76, 48 bytes

2b. Analyzing TCP packets using Wireshark:
Start your web browser and clear the browser's cache memory, but do not access any website yet.
■ Open Wireshark and start capturing.
■ Go back to your web browser and retrieve any file from a website. Wireshark starts capturing
packets.
■ After enough packets have been captured, stop Wireshark and save the captured file.
■ Using the captured file, select only those packets that use the service of TCP. For this purpose,
type tcp (lowercase) in the filter field and press Apply. The packet list pane of the Wireshark
window should now display a bunch of packets.
Part I: Connection-Establishment Phase
Identify the TCP packets used for connection establishment. Note that the last packet used for
connection establish may have the application-layer as the source protocol.
Questions
Using the captured information, answer the following question in your lab report about packets
used for connection establishment.
What are the socket addresses for each packet?
SYN: Source Address: 172.16.59.45 Destination Address: 34.120.208.123
SYN-ACK: Source Address: 34.120.208.123 Destination Address: 172.16.59.45
 ACK: Source Address: 172.16.59.45 Destination Address: 34.120.208.123.
2.What flags are set in each packet?
SYN: 0x002 (SYN) (SYN flag is set)
SYN-ACK: 0x012 (SYN-ACK) (SYN and ACK flags are set)
ACK: 0x010 (ACK) (ACK flag is set)
3.What are the sequence number and acknowledgment number of each packet?
SYN: Sequence Number (raw): 400695797 Acknowledgment number (raw): 0
SYN-ACK: Sequence Number (raw): 1761249340 Acknowledgment number (raw): 400695798
ACK: Sequence Number (raw): 400695798 Acknowledgment number (raw): 1761249341
4. What are the window size of each packet?
SYB: Window: 64240
SYN-ACK: Window: 65535
ACK: Window: 502

The data-transfer phase starts with an HTTP GET request message and ends with an HTTP OK
message.
Questions
Using the captured information, answer the following question in your lab report about packets
used for data transfer.
What TCP flags are set in the first data-transfer packet (HTTP GET message)?
Flags: 0x018 (PSH, ACK)
2. How many bytes are transmitted in this packet?	50bytes tcp payload
3. How often does the receiver generate an acknowledgment? To which acknowledgment rule
(defined in Page 200 in the textbook) does your answer correspond to?
[Time since previous frame in this TCP stream: 0.000132000 seconds]
4. How many bytes are transmitted in each packet? How are the sequence and acknowledgment
numbers related to number of bytes transmitted? 50 bytes are transmited in the GET request, and 376 bytes are received in the OK
response. The sequence number increases by the number of bytes transmited, and the
acknowledgment number increases by the number of bytes received.
5. What are the original window sizes that are set by the client and the server? Are these numbers
expected? How do they change as more segments are received by the client?
The window size when sending request to the server was set at 502. The window size
when receiving response was 256.
The window size will increase till a certain capacity
(limited by hardware) to prevent congestion.
6. Explain how the window size is used in flow control?
In a sliding window system in TCP, the size of the window is governed by 2 things:
 1.The size of the send buffer on the sending system
2. The size and available space in the receive buffer on the receiving system
To avoid congestion, the sender cannot send more bytes than the space available in the
receive buffer of the receiver. The sender must wait till the bytes in the receiving buffer have
been acknowledged. This prevents congestion, and helps in flow control.
7. What is the purpose of the HTTP OK message in the data transfer phase?
The HTTP OK message is a feedback about the request that was previously sent. An OK
response means that the request has succeeded.

Part III: Connection Termination Phase
The data-transfer phase is followed by the connection termination phase. Note that some packets
used in the connection-termination phase may have the source or sink protocol at the application
layer. Find the packets used for connection termination.
Questions
Using the captured information, answer the following question in your lab report about packets
used for connection termination.
1. How many TCP segments are exchanged for this phase?
- 4 segments are exchanged in the connection termination phase. (FIN, ACK, FIN, ACK)
2. Which end point started the connection termination phase?
- The server started the connection termination phase.
3. What flags are set in each of segments used for connection termination?
- First the server sends a segment with FIN, and ACK flags set. Then the client responds
with a segment with FIN, and ACK flags set. Then the client sends a segment with ACK
flag set, and finally the server sends a segment with FIN, and ACK flags set.
II. LAB EXERCISES
1. From the captured information, answer the following question in your lab report.
i. Using the hexdump, determine the following for any TCP packet:
The source port number, the destination port number, the sequence number, the
acknowledgment number, the header length, the set flags, the window size and the urgent
pointer value. Using the information in the detail pane lane, verify your answers is question 1.
(packet 20 of wsdata2)
Source Port: 55000 Destination Port: 80 Sequence Number (raw): 65908674
Acknowledgment number (raw): 0 Header Length: 40 bytes Flags: 0x002 (SYN)
Window: 64240 Urgent Pointer: 0
iii. Does any of the TCP packet header carry options? Explain your answer.
Using options in the TCP packet header is optional. Options are used for optimization and
are generally used in SYN packets.
iv. What is the size of a TCP packet with no options. What is the size of a TCP packet
with options?
The maximum size of the options field is 40 bytes. With option 20bytes without 12bytes
v. Is window size in any of the TCP packet zero? Explain your answer.
The window size may be zero if the receiver buffer is full, and receiver tells the sender to
keep the connection open, but not to send it anything, as it is already overwhelmed.
Once the receiver can handle more data, it can advertise a window size greater than
zero.
Another reason for window size being zero in a TCP packet could be because of the RST
flag. Sometimes connections are forcefully terminated with a packet with RST flag, and
these packets have a window size of zero